Garmin GPS to Furuno Radar

# FURUNO 000-117-603 NMEA CABLE 6 PIN

| Furuno NMEA 183 cable to Garmin 168 GPS Sounder cable |
| --- |
| Pin 1 | White | Rx+ Data1 to Garmin Tx+ (Blue) |
| Pin 2 | Black | Rx- data 1 to Garmin Tx- or its common (Black) |

| Subject |
| --- |
| I have a Garmin 168 GPS Sounder and want to connect NMEA from the GPS to the ... |
| Discussion Thread |
| Response (Leo Miranda) | 12/10/2004 03:27 AM |
| Thank you for contacting Furuno USA, Inc. Hello Roger, The NMEA # 000-117-603 cable: pin1 RX + data1 this should connect to the Garmin's TX + pin2 RX - data1 this should connect to the Garmin's TX - or it's common pin3 RX + data2 pin4 RX - data2 Sharing the same lines to the PC may cause problems as it may load down the output of the Garmin, you may need to contact them and inquire if it's ok. Or you can use a NMEA expander such as the one offer by this company: http://www.nolandengineering.com/ |
| Auto-Response | 12/09/2004 05:45 PM |
| Customer (Roger Beebe) | 12/09/2004 05:45 PM |
| I have a Garmin 168 GPS Sounder and want to connect NMEA from the GPS to the 1622. What is the pin configuration and where can I get a pigtale with the correct Furuno connector? Also, I The GPS currently is outputting NMEA data to a computer. Can I splice into the current Garmin Data cable and add the radar to the GPS data cable? |

Leo Miranda
Furuno USA, Inc.

Thank you for your inquiry.

Yes, you can splice the output line to run the NMEA data to up to 3 different devices.

Thank you and best Regards,

Stacy Derks

Product Support Specialist

GARMIN International

1200 E. 151st Street

Olathe, KS 66062  USA

http://www.garmin.com/

tel. 800/800.1020

913/397.8200

fax. 913/397.0836

-----Original Message-----

From: Roger Beebe [mailto:beebe.r@monet.k12.ca.us]

Sent: Friday, December 10, 2004 9:17 AM

To: Garmin Technical Support

Subject: Tech support request for GPSMAP 168 Sounder

Contact Information:

First Name:         Roger

Last Name:          Beebe

Address:

City, State, Zip:   , ,

Country:            United States

Phone:

E-Mail:             beebe.r@monet.k12.ca.us

Product:            GPSMAP 168 Sounder

Serial Number:      98100126

Software Version:   3.60

Problem:

NMEA output is currently connected to a computer with Mapsource software.

Can I split the connection to send NMEA data to Radar?

Request emailed to marine@garmin.com

# Text boxes

Pin 1 White

Pin 6

Pin 2 Black